Contact Robot 192.168.10.85 - UR5e

Refer Thomas’ git page to run initial scripts to setup source. Change the source location later to a folder.

# Optional conda deactivate
source devel/setup.bash

Approach 1:
run calibration
roslaunch ur_calibration calibration_correction.launch robot_ip:=192.168.10.85

run ur5e_robot bringup
roslaunch ur_robot_driver ur5e_bringup.launch robot_ip:=192.168.10.85

If this step fails with process was killed error, or any other error, follow these steps:
sudo apt update
catkin_make

After this step, Run the external command from URCaps on robot.

roslaunch robotiq_hande_ros_driver gripper_bringup.launch

##optional
roslaunch ur5e_moveit_config moveit_rviz.launch

Firewall
sudo -s
firewall-cmd --permanent --zone=trusted --add-source=192.168.10.85/24

Approach 2 (Preferred)

after calibrating do this:

Change from python to python3 in script file

# rosrun ur_robot_driver test move– for test scripts (robot_ip not needed)
rosrun ur_robot_driver test_move_delete

roslaunch robotiq_hande_ros_driver gripper_bringup.launch

To see test scripts:
/home/ise.ros/src/Universal_Robots_ROS_Driver/ur_robot_driver/scripts

Modify like that, keep in a folder and then run that script(s)

Use Logitech Camera.
OpenCV code would be separate, and it’s functions should be imported into the actual script for robot.

Cd dev/ and then ls to see the list of cameras.

How to install Gripper module:

cd /home/ise.ros/src/Universal_Robots_ROS_Driver

Then git clone the repository :
Check this repo: https://github.com/macs-lab/robotiq_hande_ros_driver

Installation should be such that ur_robot_driver and robotiq_handle_ros_driver should be in same folder

Change from python to python3 in all below script files

Change ip to 192.168.10.85 in gripper_node.py

Then roslaunch the bring up :
roslaunch robotiq_hande_ros_driver gripper_bringup.launch

then
rosrun robotiq_hande_ros_driver test_delete.py

##### Running flow

Run the Aruco.py from VS Code
Then do the ros procedures for “mess_with_This_File”